Presence sensor for ceiling installation – light and 0-10V,. 7x7m (compact office 24V lux)

Theben HTS presence sensor for ceiling installation, fully automatic with additional analogue output for SPS 0-10V, blended light measurement 10...1500 lux, range 7x7 m at installation height of 3 m, light relay: 1 floating NO contact, 2 A 24 V DC, 230 V AC, switching capacity 1 V/1 mA,  50 W/460 VA, delay 10 s...20 minutes auto-learning / short pulse, analogue output for SPS controls 0-10V for brightness: linear measuring range approx. 10-1500Lux, logarithmical approx. 10-5000Lux, remote control, front plate insulation material white 102.5x102.5x33 mm, mounting plate 70x70 mm, installation depth 40 mm

Deliver, assemble, connect up and set up

Make: Theben

Type: compact office 24V Lux

Order No.: 2014001

Unit: ST

Accessories:

# QuickSet plus

Service remote control

Order No.: 9070532

Clik

User remote control

Order No.: 9070515

# AP frame compact, white

Order No.: 9070514