Presence sensor for ceiling installation – light and HVAC,. 7x7m (compact office 24V)

Theben HTS 360° presence sensor for ceiling installation, fully automatic light control, blended light measurement  10...1500 lux, 2 relays for light and presence, range 7x7m at installation height of 3 m, light relay: 1 floating NO contact, 2 A 24 V DC, 230 V AC, switching capacity 1 V/1 mA,  50 W/460 VA, delay 10 s...20 minutes auto-learning / short pulse, presence relay: 1 floating NO contact, 2 A 24 V DC, 230 V AC, switching capacity 1 V/1 mA, 50 W/460 VA, response delay 0 s...10 minutes / room monitoring, release delay 10 s...120 minutes, remote control, front plate insulation material white 102.5x102.5x33 mm, mounting plate 70x70 mm, installation depth 40 mm.

Deliver, assemble, connect up and set up

Make: Theben

Type: compact office 24V

Order No.: 2014000

Unit: ST

Accessories:

# QuickSet plus

Service remote control

Order No.: 9070532

Clik

User remote control

Order No.: 9070515

# AP frame compact, white

Order No.: 9070514