24 V corridor presence detector for ceiling mounting, light and HVAC, 30x4m (compact passage 24 V)

Theben HTS 360° presence detector for ceiling mounting, fully automatic/semi automatic options, sensor or switch control, blended light measurement ~ 10...1500 lux, 2 relays for light and presence, rectangular detection range 30 x 4.5 m at installation height of 3 m, light relay: 1 NO contact, delay 10 s...20 min auto-learning / short pulse, presence relay: 1 NO contact, response delay 0 s...10 mins / room monitoring, fallback delay 10 s...120 mins, switching capacity of the two floating outputs 2 A/ 24 V AC/DC or 2 A/ 230V AC/DC, maximum load 50 W/460 VA, minimum load 1 V/ 1mA can be remotely controlled, front plate insulation material white 102.5 x102.5 x 44 mm, mounting plate 70 x 70 mm, installation depth 40 mm

Deliver, assemble, connect up and set up

Make: Theben

Type: compact passage 24 V

Order no.: 2014090

Unit: ST

Accessories:

# QuickSet plus

Service remote control

Order no.: 9070532

Clik

User remote control

Order no.: 9070515

# Surface (mount) frame compact, white

Order no.: 9070514