Presence detector for rack aisles and corridors, light and HKL, 15x5m (compact passimo)

Infrared - presence sensor for ceiling mounting, fully automatic/semi automatic options, sensor or switch control, blended light measurement ~ 10...1500 lux, 2 relays for light and presence, operating voltage 230V; detection area square, moving 75 m2 (15 x 5 m), stationary 50 m2 (10 x 5 m) at an installation height of 3.5 m, clear demarcation of detection area directly below presence detector; relay light: 1 NO contact 6 A 1400 VA, delay 10 s...20 min / short pulse, presence relay: 1 floating NO contact, 250 V AC, 50 W/50 VA at least 0.5 mV/10mA, delayed switch-on 0 s...10 min / room monitoring, off switching delay 10 s...120 min can be remotely controlled, front plate insulation material white 102.5x102.5x44 mm, mounting plate 70x70 mm, installation depth 40 mm

Deliver, assemble, connect up and set up

Make: thebenHTS

Type: compact passimo

Order no.: 2010080

Unit: ST

Accessories:

# Management remote control (SendoPro 868-A)

Optional for the installer for start-up or adjustment to an application. Transmission of individual settings or complete configuration sets to the detector. Saving and calling up user-defined parameter sets on internal memory or SD card. Fits all remote controlled thebenHTS presence detectors.

Order no.: 9070675

# QuickSet plus service remote control

Optional for start-up or adjustment to an application.

Order no.: 9070532

Clic user remote control

optional

Order no.: 9070515

# Surface (mount) frame compact, white

Order no.: 9070514