Digital twilight switch, 2 module, 2-99,000 lux, with wall mounted light sensor. (LUNA 111 top2 with wall mounted light sensor)

Rail mounted twilight switch; width 35 mm; separate wall mounted light sensor (IP 55); brightness range: 2 – 99,000 lux; On/Off switch delay 0-59 mins; memory card/PC interface ; external control input with 5 functions; elapsed-time counter for light sources; ON/OFF permanent; DuoFix screwless terminals; zero cross switching; 1 two way switch 16AX/250V~ sealable transparent cover

Deliver, assemble, connect up and set up

...

Make: Theben

Type: LUNA 111 top2 with wall mounted light sensor

Order no.: 111 0 100

Unit: ST

Accessories:

Terminal box cover plate

Order no.: 907 0 050

OBELISK top2 programming set

Memory card, plug-in adapter (USB), software

For Windows 2000/XP/Vista

Order no.: 907 0 409

OBELISK top2 memory card, single

Order no.: 907 0 404