Digital twilight switch, 3 module, 2- 2000 lux, digital weekly program with wall mounted light sensor. (LUNA 120 top2 with wall mounted light sensor)

Rail mounted twilight switch; width 35 mm; separate wall mounted light sensor (IP 55); analogue adjustable brightness range: 2 – 2,000 Lux; on/off switch delay 0- 59 mins; text-oriented user guidance and backlit display; weekly program; interface memory card/PC; ON/OFF permanent; instantaneous LED display; DuoFix- screwless terminals; PIN code; 10 year power reserve; zero cross switching; two way switch 16A/250V~; sealable transparent cover

Deliver, assemble, connect up and set up

...

Make: Theben

Type: LUNA 120 top2 with wall mounted light sensor

Order no.: 120 0 100

Unit: ST

Accessories:

Terminal box cover plate

Order no.: 907 0 050

OBELISK top2 programming set

Memory card, plug-in adapter (USB), software

For Windows 2000/XP/Vista

Order no.: 907 0 409

OBELISK top2 memory card, single

Order no.: 907 0 404