Digital 2 channel twilight switch, 2 module, 2-99,000 lux, weekly program with wall mounted light sensor. (LUNA 122 top2 RC with wall mounted light sensor)

Digital rail mounted twilight switch; width 35 mm; separate wall mounted light sensor (IP 55); brightness range: 2 – 99,000 lux; on/off switch delay 0-59 mins; text-oriented user guidance and backlit display; weekly program with holiday and bank holiday program; memory card/PC interface; 2 external control inputs with 5 functions; elapsed-time counter for light sources; RC DCF antenna interface; test button, ON/OFF permanent; DuoFix screwless terminals; PIN code; 10 year power reserve; zero cross switching; 2 two way switches 16A/250V~ sealable transparent cover

Deliver, assemble, connect up and set up

...

Make: Theben

Type: LUNA 122 top2 RC with wall mounted light sensor

Order no.: 122 0 100

Unit: ST

Accessories:

Terminal box cover plate

Order no.: 907 0 050

OBELISK top2 programming set

Memory card, plug-in adapter (USB), software

For Windows 2000/XP/Vista

Order no.: 907 0 409

OBELISK top2 memory card, single

Order no.: 907 0 404

top2 RC–DCF antenna

Order no.: 907 0 0011