Wall mounted twilight switch, 2-200 lux (LUNA 127 star)

Wall mounted twilight switch (IP 55); housing 85 x 118 x 49 mm; brightness range: 2 - 200 lux; preset value approx. 15 lux; on/off switch delay approx. 2-100 seconds; test button, 1 NO contact 16(10)A 230V~.

Deliver, assemble, connect up and set up

...

Make: Theben

Type: LUNA 127 star

Order No.: 1270700

Unit: ST