Wall mounted twilight switch, 2-200 lux digital with night time cut-out (LUNA 129 star-time)

Digital wall mounted twilight switch with integrated digital day time switch; IP 55; housing 85x118x49 mm; LCD display with 3 buttons; brightness range: 2 - 200 lux; preset value approx. 15 lux; on/off switch delay 0-10 minutes; 1.5 years power reserve via replaceable lithium cell, 1 NO contact 16(10)A 230V~.

Deliver, assemble, connect up and set up

...

Make: Theben

Type: LUNA 129 star-time

Order No.: 1290700

Unit: ST