Flush-mounted motion detector for wall installation, light beam, 200°, max. Ø 8m, IP40 (LUXA 103-200)

Motion detector for flush-mounted wall installation, 200° detection area, adjustable range 1-8 m radius (installation height 1.2... 2 m), upgradeable through integrated Master/Slave or Master/Master function, detection area can be limited using plug-in segments, as replacement for light or changeover switch, suitable for 50 x59 mm cover, integrated ON/AUTO/OFF switch, brightness and movement-dependent automatic switching, blended light measurement approx. 10...1000 lx, power-on time 5 s...12 min, connectable switch-off pre-warning, light relay: 1 NO contact 10 A/230V~, 1000 W incandescent lamp load, 80 x 80 mm frame, with  terminal screws.

Deliver, assemble, connect up and set up

Make: Theben

Type: LUXA 103-200

Order no.: 103 0 030

# Unit: ST

Accessories:

## RC link suppression filter

For protection against damage from power surges or switch-on (contacts) of detection sensor caused by contactors, fluorescent lamps, transformers.

250 V AC/47 Ohm, 0.1 µF

Dimensions: 24 x13 x 6mm

Order no.: 9070523