Sensor module LUXOR 411, upgrade module (LUXOR 411)

Sensor module LUXOR 411, upgrade module, rail mounted housing (4 TE), quick fastening, width 72 mm, 2 wire COM interface, 3 setting ranges 1000 -100,000 lux.,1 setting range 1 - 100 lux. Wind speed 2 - 20 m/s. Temperature range 0°C - 60°C, switch on/off delay 80 seconds. Connection options: max. 3 mounted light sensors and 1 wind sensor or 1 LUXOR 412 weather sensor system and max. 2 mounted light sensors. LED display of threshold values. Operating voltage 230V~, 50Hz.

Deliver, assemble, connect up and set up

...

Make: Theben

Type: LUXOR 411

Order No.: 4110000

Unit: ST