Central display and control unit for LUXOR (LUXOR 426)

Display with multi-function in extremely flat glass design; flush-mounted installation; panel 128 x 93 x 15 mm; colour white; display with 6 different illuminated display pages each with 8 lines; time, weekday, date as well as central and automatic functions are displayed; current weather conditions are displayed as well as min./max values in combination with LUXOR 411 and 412; display backlighting; favourite sites can be selected from 6 pages; 8 channel time switch, in combination with a RAMSES room thermostat for heating - temperature reduction. Daily and weekly programming; manual switching on the device for central and group functions as well as manual and automatic mode; daily and weekly programs; astronomical program (dependent on sunrise and sunset); freely programmable switching times as well as pre-programmed astronomical switching times; offset settings +- 120 min.; location input via city list; individual link of time switch channels with the outputs possible; Z	Positioning of drives (LUXOR 408/409) as well as transmission of dimming values (LUXOR 405) as percentage values; Blocking times for suppression of brightness or twilight signals from sensor module (LUXOR 411); Astronomical blocking times for time shifts for moving shutters/awnings up and down; automatic daylight savings time switchover; PIN code; COM connection and 230V~ connection.

Deliver, assemble, connect up and set up

...

Make: Theben

Type: LUXOR 426

Order no.: 4260000

Unit: ST