KNX presence detector, flush-mounted installation in concrete ceiling, (PlanoCentro UWH-A-KNX)

Passive infrared (PIR) presence detector for flush-mounted installation in concrete ceiling; flush fitting, with metal installation frame for screw attachment in flush-mounted socket for concrete ceiling or wooden ceiling; flush-mounted socket: e.g. connection box/flush-mounted junction box Agro/Kaiser 115x115x100 (LxWxD);

Two light channels for controlling two lighting groups; switching or constant light control; channel brightness with cyclical output; channel for room monitoring;  can be operated semi or fully automatically; reduction of lighting time delay in event of brief absence; mixed light measurement 5-2000 lx,; square 360° detection area max. moving 100m2 (10x10 m) stationary 64m2 (8x8 m) at 3.5m installation height; light switch-off delay auto-learning 30 s...60 min, switching between 2 brightness set point values, brightness set point values can be adjusted via bus, standby function; presence channel with switch-on delay 10 s...30 min / inactive, switch-off delay 10 s...120 min; parameters can be set and read remotely (SendoPro 868-A), Master/Slave mode option; test functions; scene control with two scenes, 8-bit scenes; white front frame 123 x123 x 6 mm, device installation depth 90 mm; IP 40 protection rating; integrated bus coupling unit and power supply via bus.

Excluding install and start up.

Make: ThebenHTS

Type: PlanoCentro UWH-A KNX, white

Order no.: 2059202

Unit: ST

Accessories:

# Management remote control (SendoPro 868-A)

Optional for the installer for start-up or adjustment to an application. Text-based operator guidance in the display. Transmission of individual settings or complete configuration sets to the detector possible. Saving and calling up user-defined parameter sets on internal memory or SD card. Fits all remote-controlled ThebenHTS presence detectors.

Order no.: 9070675

SendoClic user remote control

optional

Order no.: 9070690