Presence detector, flush-mounted installation in concrete ceiling, (PlanoCentro 101-UWH)

Passive infra-red presence detector for flush-mounted installation in concrete ceilings; flat design with metal installation frame for screwed fixing in wooden or concrete ceilings; flush-housing installation depth 100x100 mm; switchable between fully automatic/semi automatic, sensor or switch control, blended light reading 5-2000 lux, 2 relays for light and presence; operating voltage 230V; square 360° detection range max. moving 100 2 (10x10 m) stationary 64 m2 (8x8 m) at 3.5 m installation height; relay light: 1 NO contact 10 A 2300 VA, off switching delay 10 s...60 min / short pulse; presence relay: 1 floating NO contact, 60 W /220 V DC  and/or 62 VA/ 250V AC at least 0.5 mV/10mA, delayed switch-on 0 s...10 min / room monitoring, off switching delay 10 s...120 min, 6 factory settings or remote operation parameter, Parameters can be selected, front frame white 123 x123 x 6 mm, device installation depth 90 mm; protection rating IP 40

Install and start up.

Make: thebenHTS

Type: PlanoCentro 101-UWH

Order no.: 2030202

Unit: ST

Accessories:

# Flush-mounted junction box

Kaiser 115 x 115 x 100 mm, 1298-07

Order no.: 9070689

# Management remote control (SendoPro 868-A)

For the installer for start-up or adjustment to an application. Text-based operator guidance in the display Transmission of individual settings or complete configuration sets to the detector possible. Saving and calling up user-defined parameter sets on internal memory or SD card. Fits all remote controlled thebenHTS presence detectors.

Order no.: 9070675

SendoClic user remote control

Optional order no.: 9070515