# Tender text for presence detectors

# Presence detectors for ceiling installation PlanoCentro 300 EWH / EBK / ESR

Passive infrared presence detectors for hollow ceiling installation; flat design; square 360° detection area, walking 100 m2 (10 x 10 m), sitting 64 m2 (8 x 8 m) at 3.5 m installation height;

Automatic presence and brightness-dependent control for lighting and HVAC; can be switched between fully automatic or semi-automatic operation; mixed light measurement approx. 10 - 2000 Lux;

Operating voltage 230 V AC /50 Hz;

Channels A, B, C light: relay closer, 230 V / 10 A, 2300 W, zero cross switching, switch-off delay 10 s – 60 min, staircase light function, connection option for push buttons or switches for manual switching, with automatic recognition of push button/switch;

6 defined parameter basic settings direct on the device, configurable sensitivity; remotely configurable and reading of the set parameters;

Installation cut-out section 100 x 100 mm, cover white 112 x 112 x 5 mm, can be changed according to design, colour and material; protection rating IP 40 in fitted state

Manufacturer: thebenHTS

Type: PlanoCentro 300 E..

Order No.:	203 0 302 (PlanoCentro 300-EWH, white, similar to RAL 9010)

203 0 303 (PlanoCentro 300-EBK, black, similar to RAL 9005)

203 0 304 (PlanoCentro 300-ESR, silver, similar to RAL 9006)

Unit: ST

### Accessories

### SendoPro 868-A management remote control

Optional for the installer for start-up or adjustment to usage conditions.

Text-based operator guidance in the display. Transmission of individual settings or complete configuration sets to the detector possible. Option of calling up pre-defined parameter sets. Suitable for all remote controlled thebenHTS presence detectors.

Order no.: 907 0 675

### SendoClic user remote control

optional

Order no.: 907 0 690