Presence sensor for ceiling installation, maximum 7x7 m (Presence Light 360)

Theben HTS presence sensor 360° for ceiling installation, fully automatic light control, blended light measurement  10...1500 lux, 1 light relay, square detection area 7x7m, installation height 3.0 m, 8x8m, installation height 3.5 m, light relay: 1 NO contact 6 A 1400 VA, delay 10 seconds...20 minutes auto-learning / short pulse, protection class IP54, can be remotely operated, front plate insulation material white 86x86x27 mm, mounting plate 70x70 mm, installation depth 40 mm

Deliver, assemble, connect up and set up

Make: Theben

Type: Presence Light 360

Order No.: 200 0 050

Unit: ST

Accessories:

# QuickSet plus

Service remote control

Order No.: 9070532

Clik

User remote control

Order No.: 9070515

# AP frame Presence Light, white

Order No.: 9070513