KNX presence detector; ceiling installation, pure white, 2x light / 2x presence

(PresenceLight 360B-KNX WH)

Passive infrared (PIR) presence detector for ceiling installation; fully automatic light control; can be operated semi or fully automatically; manual push button control; mixed light measurement 5-2000 lx,;

square 360° detection area max. moving range 49 m2 (7x7 m) stationary 20 m2 (4.5x4.5 m) at 3 m installation height; 1 or 2 light channels for controlling two lighting groups; switching or constant light control; Light- switch-off delay auto-learning 30 s...60 min, switching between 2 brightness set point values, brightness set point values can be adjusted via bus, standby function; channel brightness with cyclical output; channel for room monitoring; reduction of lighting time delay in case of short presence; presence channel with switch-on delay 10 s...30 min / inactive; switch-off delay 10 s...120 min; can be remotely operated; Master/Slave mode option; test functions; scene control with two scenes, 8-bit scenes; protection class IP54; integrated bus coupling unit and power supply via bus; front plate insulation material white 86x86x27 mm, mounting plate 70x70 mm, installation depth 38 mm;

Excluding install and start up.

Make: ThebenHTS

Type: PresenceLight 360B-KNX WH, white

Order no.: 2009000

Unit: ST

Accessories:

# Management remote control (SendoPro 868-A)

Optional for the installer for start-up or adjustment to an application. Text-based operator guidance in the display. Transmission of individual settings or complete configuration sets to the detector possible. Saving and calling up user-defined parameter sets on internal memory or SD card. Fits all remote-controlled ThebenHTS presence detectors.

Order no.: 9070675

SendoClic user remote control

optional

Order no.: 9070690

# AP frame Presence Light, white

Order No.: 9070513

# Protective cage QuickSafe

Order No.: 9070531