Clock thermostat 24 hour and 7 day program, operating mode switch, 2 wire (RAM 784)

Electronic thermostat with automatic night temperature reduction; adjustable for daily and weekly program; programmable every 5 minutes or 30 minutes; shortest switching time for weekly program 2 hours; day and night temperature settings from +10°C ... 30°C; operating mode selector switch; frost protection 6°C; party switch; indicator display; thermal circulation and operating point settings; silting and pump protection function can be activated; connection for telephone remote switch; housing colour: white; 1 two way switch 6A/250V~.

Deliver, assemble, connect up and set up

...

Make: Theben

Type: RAM 784

Order No.: 7840030

Unit: ST