Digital clock thermostat, 7 day, text line, 2 wire (RAM 831 top 2(with batteries))

Elegantly designed digital room thermostat; info button for important information; text line in the display with step-by-step operator guide; illuminated display through keystroke; weekly program; switch for 3 basic programs with modifiable temperatures and with up to 42 time/temperature phases; setting range +6°C ... 30°C in 0.2 degree increments; 3 comfort and 2 reduction programs can be allocated to each phase; optimisation function for automatic  correction of heating start up; external input for connection of presence detectors, floor sensors ,window contacts or telephone remote switches; date-controlled holiday program; fully automatic summer/winter time changeover; party and ECO program with adjustable duration; frost protection a summer switching; operating point and switching differential can be adjusted; power supply via two 1.5 V AA alkaline batteries; low battery indication. Housing colours: white; 2 point control; 1 two way switch 6 A/250 V~.

Deliver, assemble, connect up and set up

...

Make: Theben

Type: RAM 831 top 2(with batteries)

Order No.: 8319132

Unit: ST