Presence detector for ceiling installation, light beam, 360°, max. Ø 6 m, IP 41 (SPHINX 104-360)

Presence detector for ceiling installation on flush-mounted socket, 360° detection area, detection radius 6..-7 m (installation height  2.5 m), detection area can be limited using segments; internal installation (IP41), brightness and presence-dependent automatic switching, blended light measurement approx. 10...2000 lx, power-on time 1 s...20 min or pulse 1 s, light relay with zero cross switching: 1 NO contact 8 A/230V~, 1800 W incandescent lamp load, external switch, Master/Slave switching, white housing 110x110x53 mm, plug-in base with screwless terminals.

Deliver, assemble, connect up and set up

Make: Theben

Type: SPHINX 104-360

Order no.: 104 0 370

# Unit: ST

Accessories:

Service remote control

for easy setting or subsequent correction of parameters.

Teach-in function for current brightness.

Type: SPHINX RC 104 pro

Order no.: 9070536

User remote control

for easy ON / OFF /AUTO manual switching.

Teach-in function for saving current switching brightness.

Type: SPHINX RC 104

Order no.: 9070538

## RC link suppression filter

For protection against damage from power surges or switch-on (contacts) of detection sensor caused by contactors, fluorescent lamps, transformers.

250 V AC/47 Ohm, 0.1 µF

Dimensions: 24 x13 x 6mm

Order no.: 9070523