Rail mounted 7 day timer, segments, power reserve, 3 TLE (SUL 191 w)

Rail mounted time switch with approx. 200 hour power reserve; width 52.5 mm; 7 day program; shortest switching time 2 hrs.; clock hand for time display and 12/24 hour recognition; time can be adjusted clockwise or counter-clockwise; switching pre-selection; manual switch with 3 positions: Continuous ON/AUTO/continuous OFF; switching status display; DuoFix spring terminal for 2 conductors; 1 two way switch 16 A /250 V~; 230V / -50 Hz;sealable transparent cover.

Deliver, assemble, connect up and set up

...

Make: Theben

Type: MEM 191 w

Order no.: 1910011

Unit: ST