# Tender text for motion detector

# Motion detector theMova S360 KNX AP WH / GR

Passive-infrared motion detector for ceiling installation; surface-mounted; automatic motion and brightness-dependent control for lighting and HVAC; round 360° detection area, walking up to 64 m2 (Ø 9 m), installation height up to 4 m;

Mixed light measurement suitable for fluorescent lamps (FL/PL/ESL), halogen/incandescent lamps and LEDs;

Energy consumption approx. 8 mA / 9 mA with LED on; protection rating IP 54; operating temperature -15° C to +50° C;

1 channel for light C1, switched mode; can be switched for operation as fully or semi-automatic; brightness switching value adjustable in lux via parameter, object or remote control; teach-in of brightness switching value; reduction of time delay during brief presence (temporary presence); manual override by means of telegram or remote control;

1 channel presence for C4, switch-on delay and time delay configurable;

Separate disable object for light and presence channel; recording and transmitting of the current brightness; configurable sensitivity; test mode to check function and detection area; extension of detection area by parallel switching of several motion detectors (master / slave or master / master); can be configured remotely with remote control.

Manufacturer: 	thebenHTS

Type: theMova S360 KNX AP..

Order no.: 1039550 (theMova S360 KNX AP WH, white)

1039551 (theMova S360 KNX AP GR, grey)

Unit: ST

### Accessories

### Management remote control "SendoPro 868-A"

Optional

For the installer for start-up or adjustment to usage conditions.

Text-based user guidance in the display. Transmission of individual setting values or complete parameter sets to the detector possible. Suitable for all remote controlled thebenHTS presence and motion detectors.

Order no.: 9070675

### Service remote control "theSenda P"

Optional

Order no.: 9070910

### User remote control "theSenda S"

Optional

Order no.: 9070911